YOUR COMPANY NAME HERE

# EXAMPLE SITE QUALITY CHECKLIST & COMPLETION HANDOVER SHEET

| Date of Inspection/Check: | Job Reference: |
| --- | --- |
| Customer Company Name: | Site Name/Address: |
| Customer Representative: | AlphaFence Representative: |
| Date Job Started: | Date Completed: |
| Brief Description of Works: |
| Description/Item: | ( | Comments: (“N/A” if not applicable) |
| Posts: |  |  |
| Posts stable: adequate sized footings, and concrete fully set |  |  |
| Posts vertical |  |  |
| Posts inline |  |  |
| Post tops follow ground contours, or straight between (as spec.) |  |  |
| Mesh: |  |  |
| Mesh tight and joined/overlapped securely |  |  |
| Mesh Panels Secured Tightly (Note Cut Ends) |  |  |
| Stretcher Bars/Bolts Tight and Secure |  |  |
| Wire ties at correct BS centres: 150/450/300 mm top/mid/bottom |  |  |
| Security cleats installed: corners/ends (two per post) |  |  |
| Barbed wire attached and tight |  |  |
| Line-wires tight; bare/stripped areas painted/replaced |  |  |
| Gates: | : |  |
| Gate drop-sockets and sleeves in place: open/closed |  |  |
| Drop-bolts long enough to reach floor (and can’t be removed) |  |  |
| Anti-lift pins/mechanism fitted to gate leaves |  |  |
| Gates adjusted to open/close over ground, and lock smoothly |  |  |
| Sharp burrs removed from drop-bolts and latch area |  |  |
| Gate posts/latches/frame touched up |  |  |
| Gate eyes/hinges tightened, cut off and secured |  |  |
| Adjacent fence/panels attached securely and appropriately |  |  |
| General: |  |  |
| Concrete/earth splashes cleaned from bottom of all posts/panels |  |  |
| All cuts/holes de-burred and/or touched up |  |  |
| All rubbish, packaging, off-cuts, pallets removed from site |  |  |
| All spoil spread/removed from site, or holes reinstated as contract |  |  |
| Gaps/holes beneath fence filled with spoil |  |  |
| Temporary panel clips/stays/braces etc removed from fence/site |  |  |
| Nuts/bolts/rivets tightened/snapped-off (debris removed) |  |  |
| Palisade legs installed (if required) |  |  |
| Hired plant off-hired |  |  |
| Company Fence Signs attached: entrances, corners, and at 50 m |  |  |
| List Below any remedial works/snagging requiring completion before handover and acceptance: |
| Item | Description | ( |
| 1 |  |  |
| 2 |  |  |
| Signed in Agreement and Acceptance of the completed works: Signature: Name (print): Date |